- Purpose

- To establish the system to inspect and maintain vehicles and heavy construction equipment.

- Responsibility

  - The Key Supervisor shall be responsible for the following:

    - Maintaining vehicles and equipment in accordance with applicable Occupational Safety and Health Administration/Department of Safety and Health (OSHA/DOSH) and American National Standards Institute (ANSI) standards.

    - Conducting inspections of equipment, and correcting deficiencies noted during the inspections.

  - Employees shall be responsible for conducting daily inspections of equipment they are operating, and for reporting deficiencies to their supervisor.

- Definitions

- Heavy Construction Equipment:  Tractors, compactors, fork lifts, graders, scrapers, off-highway trucks, etc.

- Motor Vehicles:  Any vehicles that operate on a construction site.

- Preventive Maintenance:  Practice of utilizing periodic inspections, adjustments, lubrication, and minor repair of equipment for the purposes of extending its useful life and reducing the frequency and magnitude of repairs.

- Scheduled Maintenance:  Regularly scheduled inspections, tests, lubrications, adjustments, cleaning, and tightening of various components of a piece of equipment.

- General Requirements

  - Equipment maintenance and inspection shall comply with the following statutory requirements:

- 29 Code of Federal Regulations (CFR) 1926, Subpart O; Motor Vehicles, Mechanized Equipment and Marine Operations

- 29 Code of Federal Regulations (CFR) 1910, Subpart N; Materials Handling and Storage

- 29 Code of Federal Regulations (CFR) 1910, Subpart F; Powered Platforms, Manlifts, and Vehicle-Mounted Work Platforms

- Washington Administrative Code (WAc) 296-155, Part M; Motor Vehicles, Mechanized Equipment and Marine Operations.

  - On-site preventive maintenance of equipment and vehicles shall be performed by qualified personnel.

  - Motor vehicles and heavy equipment shall be maintained and inspected monthly in conformance to the manufacturer’s recommendations, and documented on equipment-specific safety check and/or inspection report forms (see attachments 19-A).

  - Prior to heavy equipment being brought onto a project, an inspection of the equipment shall be performed and complete the applicable safety check and inspection report forms.  The forms shall be submitted to maintenance department.  Deficiencies noted during the inspection shall be corrected prior to the equipment being brought onto the project.

  - Apollo shall notify the owner or general contractor when heavy equipment is to be brought onto a project.

  - The key supervisor shall maintain manufacturer’s recommendations and inspection checklists onsite for review.

- Procedure

  - Motor Vehicles

    - Vehicles being operated shall be checked at the beginning of each shift to ensure that the following parts, equipment, and accessories are in safe operating condition and free of apparent damage that could cause failure while in use.

- Brakes (including trailer brake connections, parking brake, and emergency stopping systems.

- Tires

- Horn

- Steering mechanism

- Coupling devices

- Seat belts

- Operating controls

- Safety devices

    - Lights, reflectors, windshield wipers, defrosters, fire extinguishers, steps, and hand-holds for vehicle access shall also be inspected where such equipment is necessary.

5.1.3	Defects noted during the motor vehicle inspection shall be corrected before the vehicle is placed into service.

  - Heavy Construction Equipment:  The following are specific requirements relating to heavy equipment.

    - Crawler, locomotive, and truck cranes shall be inspected in accordance with AISH-36

    - Lift Trucks:  Operation of powered industrial trucks may be hazardous if maintenance is neglected or repairs, rebuilds, or adjustments are not performed in accordance with the manufacturer’s design criteria.

      - A scheduled, planned maintenance, lubrication, and inspection system shall be followed on all powered industrial trucks.

      - In an industrial truck is found to be in need of repair or is in any way unsafe or contributes to an unsafe condition, the truck shall not be operated until it has been restored to safe operating condition.

      - Only qualified operators are allowed to operate lift trucks.

6.0	Records

| Document | Record Submittal Responsibility | Record Retention Responsibility |
| --- | --- | --- |
| Lift Trucks Inspection | Contractor | Apollo |
| Earthmoving Equipment Inspection | Contractor | Apollo |
| Miscellaneous Equipment Inspection | Contractor | Apollo |
| Manlift Inspection | Contractor | Apollo |

7.0	References

ANSI A92.6			Self-propelled Elevating Work Platforms

ANSI A92.5			Boom Supported Elevating Work Platforms

ANSI/ASME B56.1a	Safety Standards for Low Lift And High Lift Trucks

ANSI/ASME B30.5	Mobile And Locomotive Cranes

8.0	Attachments

AISH 19-A	Lift Truck Inspection

AISH 19-B	Earth Moving Equipment Inspection

AISH 19-C	Miscellaneous Equipment Inspection

AISH 19-D	Manlift Inspection

APOLLO MANLIFT INSPECTION

PROJECT:___________________________

MAKE:______________________MODEL:________________EQUIPT. #_________MAX Capacity:________________

INSPECTOR:________________________SUPERVISOR:______________________

| Item | Mon | Tues | Wed | Thurs | Fri | Sat | Sun |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  | YES | NO | YES | NO | YES | NO | YES | NO | YES | NO | YES | NO | YES | NO |
| Lift capacity displayed |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Load chart displayed and legible |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Warning stickers and control stickers legible |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Fire extinguisher provided and in working order |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Are all posted warnings visible |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Equipment free from leaks |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Guardrails in good condition |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Warning light work |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Alarms work if required |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Safety harness attachment point in good condition |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Out riggers in good condition |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Exposed parts guarded |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Controls working properly |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Operations/maintenance manuals available |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Spill containment Diaper in working condition |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Is manlift mechanically sound |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Is manlift safe to operate. |  |  |  |  |  |  |  |  |  |  |  |  |  |  |

Note: If items do not apply place a N/A in check box. If any problems notify supervisor immediately.

Comments:

APOLLO

EARTHMOVING EQUIPMENT INSPECTION

PROJECT:________________________PROJECT #:__________DATE:__________

TYPE OF EQUIPMENT:_________________________________________________

MAKE:______________________MODEL:__________________EQUIPT. #:______

INSPECTOR:________________________SUPERVISOR:______________________

ITEM                                      YES   NO   N/A         DATE CORRECTED

BY WHOM

- Is manufacturer operations and

maintenance data available?____________________________________________

- Are maintenance and inspection

records available?_____________________________________________________

- Is a fire extinguisher provided?___________________________________________

- Are tools & equip. secured?_____________________________________________

- Are seat belts provided?________________________________________________

- Is Roll Over Protective System

provided in good condition?_____________________________________________

- Are windshield/windows, safety

glass and in good condition?_____________________________________________

- Are brakes in good working order?________________________________________

- Are auxiliary brakes provided &

working?____________________________________________________________

- Bi-directional audible alarm?____________________________________________

- Back-up audible alarm?_________________________________________________

- Are all lights operable?_________________________________________________

- Are moving parts guarded?______________________________________________

- Are hydraulic lines in good

condition?____________________________________________________________

- Are lifting cables, winch lines, etc.

in good operable condition?_____________________________________________

- Are tires in good condition?_____________________________________________

- Are all fluid levels good?________________________________________________

REMARKS:_____________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________

MISC EQUIPMENT INSPECTION

INSPECTED BY:_______________________________________DATE:____________

MAKE:______________________MODEL:_____________________YEAR:________

EQUIPMENT #:______________LICENSE #:_________________EXPIRES:________

INSPECTOR:_______________________SUPERVISOR:________________________

PROJECT/DEPARTMENT:________________________________________________

ITEM                                     GOOD    BAD      N/A     DATE CORRECTED

(by whom)

HEADLIGHTS___________________________________________________________

TAILLIGHTS____________________________________________________________

TURN SIGNALS_________________________________________________________

BRAKE LIGHTS_________________________________________________________

4-WAY FLASHERS_______________________________________________________

HORN__________________________________________________________________

BACK-UP ALARM_______________________________________________________

SEAT BELTS____________________________________________________________

WINDOW GLASS________________________________________________________

WIPERS________________________________________________________________

INTERIOR______________________________________________________________

EXTERIOR______________________________________________________________

FIRE EXTINGUISHER____________________________________________________

FIRST AID KIT__________________________________________________________

BRAKES________________________________________________________________

PARKING BRAKE_______________________________________________________

TIRES__________________________________________________________________

RUNNING CONDITION___________________________________________________

FLUID LEAKS___________________________________________________________

CLEAN & ORDERLY_____________________________________________________

GENERAL CONDITION___________________________________________________

OTHER:________________________________________________________________

LAST MAINTENANCE, if known (lube,oil,tune-up,etc.) Date:_____________________

REMARKS:_____________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________